## Slide 1
BL
CompTIA Security+ SY0-701
VPN & Remote Access
IPSec · SSL VPN · Split Tunnel · SD-WAN · ZTNA
BL Cybersecurity Series · Study Presentation

## Slide 2
VPN Types
Site-to-Site VPN
Connects two office networks permanently
Replaces expensive MPLS circuits
IPSec tunnel between gateways
Transparent to end users
Always-on; no client required
Example: Branch office to HQ
Remote Access VPN
Individual user connects to corporate network
Client software on laptop/phone
Full tunnel: all traffic through VPN
Split tunnel: only corporate traffic through VPN
SSL/TLS VPN: uses HTTPS (port 443)
Examples: Cisco AnyConnect, GlobalProtect
BL Cybersecurity Series · CompTIA Security+ SY0-701

## Slide 3
IPSec Framework
IPSec — Suite of protocols for securing IP communications
AH (Authentication Header) — Provides integrity and authentication; NO encryption
ESP (Encapsulating Security Payload) — Provides encryption + integrity + authentication
IKE (Internet Key Exchange) — Negotiates security parameters and exchanges keys
TUNNEL MODE — Encrypts entire IP packet; used for site-to-site VPN
TRANSPORT MODE — Encrypts payload only; used for host-to-host within same network
IKEv2 — Faster reconnection, MOBIKE for roaming; preferred for mobile devices
BL Cybersecurity Series · CompTIA Security+ SY0-701

## Slide 4
Modern Remote Access: ZTNA vs VPN
SPLIT TUNNELING — Risk: user traffic bypasses corporate controls; malware can enter
FULL TUNNEL — All traffic inspected; slower but more secure
SD-WAN — Software-Defined WAN; intelligent routing across multiple links
ZTNA (Zero Trust Network Access) — Application-level access; never exposes network
ZTNA vs VPN: ZTNA grants access to specific apps; VPN grants access to whole network
CASB — Cloud Access Security Broker; security between users and cloud apps
Always-on VPN — Client connects automatically; cannot be disabled by user
BL Cybersecurity Series · CompTIA Security+ SY0-701

## Slide 5
KEY TAKEAWAYS
VPN & Remote Access
1
IPSec ESP provides encryption + integrity; AH provides only integrity (no encryption)
2
Split tunneling improves performance but creates security risks — evaluate carefully
3
ZTNA is replacing traditional VPN — grants per-app access, not full network access
4
IKEv2 with MOBIKE enables seamless VPN reconnection when network changes
5
SD-WAN provides cost-effective site connectivity with intelligent traffic routing
BL Cybersecurity Series · CompTIA Security+ SY0-701